## Slide 1
ADVANCED COMPUTER ARCHITECTURES
Conversational QoR Debugging Agent
for Open ASIC Flows
A conversational tool for understanding LibreLane/OpenROAD physical-design reports
Marat Yerkebayev Aigerim Turazhanova
Politecnico di Milano Academic Year 2025–2026

## Slide 2
CONVERSATIONAL QoR DEBUGGING
Why QoR debugging is harder than it looks
02
THE ANALYSIS BURDEN
The information is scattered
JSON metrics and text reports must be combined before we can see the full timing, power, area and routing picture.
Each corner tells a different story
Setup and hold results change with process, voltage and temperature—and WNS, WS and slack are easy to mix up.
Timing is only part of the picture
Electrical, utilization and routing problems may still remain after setup timing passes.
PROJECT OBJECTIVE
Make the reports easier to understand—and easier to trust.
Our assistant collects the QoR metrics, points to the most important blocker and explains the answer using evidence from the reports.
Faster diagnosis · fewer interpretation errors · reproducible decisions

## Slide 3
CONVERSATIONAL QoR DEBUGGING
PM32 connects an architecture decision to a real timing limit
03
Execution Time
=
Instruction Count
×
CPI
×
Clock Period
limited by physical implementation
32-bit operand A
SERIAL–PARALLEL MULTIPLIER
64-bit result
32-bit operand B
IDLE
RUNNING
64 cycles
DONE
Lower complexity, shorter combinational path
Trade-off: smaller area potential, but 64-cycle execution latency.
How far can we reduce the clock while keeping timing, power, area and routing under control?

## Slide 4
CONVERSATIONAL QoR DEBUGGING
We explored ten clock periods, but only four runs completed
04
CLOCK PERIOD EXPLORATION (ns)
8
failed
10
failed
11
complete
12
complete
15
config only
18
config only
20
config only
22
config only
25
complete
30
complete
ENVIRONMENT
LibreLane / OpenROAD
v3.0.3
Sky130 PDK
sky130_fd_sc_hd
Evidence scope
4 complete runs
No global optimum is claimed until the remaining configurations are executed.

## Slide 5
CONVERSATIONAL QoR DEBUGGING
Here is how a question becomes a traceable answer
05
Every answer starts from the reports—not from the language model.
01
RTL + clock config
02
LibreLane / OpenROAD
03
Deterministic parser
04
Structured QoR dataset
05
Rule-based diagnosis
06
Conversational assistant
07
Optional validated LLM
Parse first → diagnose second → explain last

## Slide 6
CONVERSATIONAL QoR DEBUGGING
We keep the raw metrics, timing meaning and diagnosis separate
06
37
normalized fields per run
Timing • setup + hold WNS and WS • normalized margins • worst PVT corners Physical QoR • power + area + utilization • slew, capacitance, fanout • DRC, wirelength, vias Trust • source files + confidence • parser warnings
WNS = 0 ns
No negative setup violation
WS > 0 ns
Positive worst-slack margin
This prevents us from calling WS “positive WNS.”
SUPPORTED NUMBERS ONLY
The LLM can explain a result, but it cannot change the numbers.
WHAT WE FIX FIRST
1
DRC errors
2
Hold failure
3
Setup failure
4
Electrical violations
5
Congestion / utilization
6
Clock optimization
We only tighten the clock after the blocking physical problems are resolved.

## Slide 7
CONVERSATIONAL QoR DEBUGGING
The assistant finds clock_11—and explains the remaining risks
07
“What is the fastest setup-clean run?”
Assistant answer
clock_11
smallest completed run that meets setup timing
11 ns
clock period
1.237 ns
setup margin
0.119 ns
hold margin
0
routing DRC errors
3.371 mW
total power
WHY IT IS NOT QoR-CLEAN
247 slew violations · 1 fanout violation · 85.2% utilization
So the next step is to fix the electrical and utilization blockers before reducing the clock again.

## Slide 8
CONVERSATIONAL QoR DEBUGGING
As the clock gets faster, power rises and timing margin shrinks
08
MEASURED POWER ACROSS COMPLETED RUNS
Completed-run evidence
Run
Period
Setup slack
Power
clock_11
11 ns
1.237 ns
3.371 mW
clock_12
12 ns
3.237 ns
2.809 mW
clock_25
25 ns
13.237 ns
1.348 mW
clock_30
30 ns
17.237 ns
1.124 mW
3.0×
higher power at 11 ns than at 30 ns
15,942.8 µm²
area remains approximately constant
Chart: Clock period (ns)
| 11 | 12 | 25 | 30
Total power (mW) | 3.371 | 2.809 | 1.348 | 1.124

## Slide 9
CONVERSATIONAL QoR DEBUGGING
Every planned test passed, with a clearly defined scope
09
We tested the project at four levels: code, conversation, decision logic and reproducibility.
110
unit + integration tests
Parser, rules, assistant, LLM validation, discovery and Pareto logic
✓
24/24
conversation scenarios
Natural language, missing data, WNS/WS, congestion and hallucination checks
✓
18/18
decision-logic scenarios
Synthetic combinations verify the recommendation hierarchy
✓
10/10
project validation checks
Compilation, schema, semantics, docs, status and reproducibility
✓
Scope note: 100% means all predefined scenarios passed—not a statistical guarantee for every possible question.

## Slide 10
CONVERSATIONAL QoR DEBUGGING
We show what the data can prove—and what it cannot
10
RELIABILITY MECHANISMS
• Never invent a missing metric • Separate completed, failed and config-only runs • Reject unsupported numerical claims • Track the source file for important evidence • Keep DRC and congestion conclusions distinct
0 final DRC errors ≠ 0 congestion
Global-routing overflow metrics are required to quantify congestion.
WHAT WE KNOW TODAY
4 / 10
complete configurations
• One benchmark: PM32 • CLI-only interface • No explicit overflow data • No per-path timing analysis • Limited conversation memory • Auto-tuning needs a live flow
WHAT WE WOULD DO NEXT
Run all clocks
Add benchmarks
Analyze paths
Parse congestion
Build dashboard
Auto-tune constraints
The most useful next step is simple: run the six missing clock configurations.

## Slide 11
CONCLUSION
QoR tells us whether an architecture target is physically realistic
FASTEST COMPLETED SETUP-CLEAN RUN
clock_11
11 ns clock · 1.237 ns setup margin
Not fully QoR-clean: 247 slew violations, 1 fanout violation and 85.2% utilization.
WHAT WE BUILT
Deterministic 37-field parser Correct WNS / WS semantics Explainable diagnosis hierarchy Evidence-linked conversational answers Validated optional LLM wording Reproducible test framework
Architecture sets the target. Physical implementation tells us whether the design can actually reach it.
11